Explanation on the
startup_TRB49.sh script
 Sequence of commands and details on the required files

The script called to startup TRB3 and initialize ADC AddOns is startup_TRB49.sh[1]
[1] A copy of the startup_TRB49.sh script is available in this document.

[Local reference: /home/odroid/trbsoft/userscripts/trb49/]

The file can be downloaded from the repository (inside the directory /userscripts_trb49_on_control_unit_OdroidC2):
https://github.com/jsmarcos/TRB3-GSI-based-DAQ

Direct link: https://raw.githubusercontent.com/jsmarcos/TRB3-GSI-based-DAQ/master/userscripts_trb49_on_control_unit_OdroidC2/startup_TRB49.sh

It sends the configuration of several parameters in the FPGA and ADC AddOns of TRB3 board, throught the application ‘trbcmd’, which sends commands to TRB3.

→ Four operations executed by the startup_TRB49.sh script:

1) Check if there is communication with TRB3 board, reset the system and ask for the available “endpoints” (FPGAs). This is done through two Perl scripts: check_ping.pl and trbreset_loop.pl refered to below.

2) Set the name of the available FPGAs (confirm)

3) Set the GbE settings throught the Perl script loadregisterdb.pl, taking the required information from Perl database (text files). Example of a setting: IP addresses and ports of the machine that will recieve the .HLD files with the channels waveforms.

Below are the Perl command used in the startup_TRB49.sh script[2]:
[2] The databases (.db files) passed as argument of the Perl scripts are copied in the end of this document.

loadregisterdb.pl db/register_configgbe.db	# must be changed accordingly (ID of the CTS_FPGA as defined above)
loadregisterdb.pl db/register_configgbe_ip.db	# must be changed accordingly (DAQ_MAC + IP + Dest Port (used in EventBuilder_TRB186.xml))

#echo "TDC settings"
loadregisterdb.pl db/register_configtdc.db

Note that in the beginning of the startup_TRB49.sh script the path for the Perl application loadregisterdb.pl is defined, through the commands:

DAQ_TOOLS_PATH=~/trbsoft/daqtools
export PATH=$PATH:$DAQ_TOOLS_PATH
export PATH=$PATH:$DAQ_TOOLS_PATH/tools

In the current software installation, the Perl databases are saved in a directory “db”, inside the startup_TRB49.sh:

/home/odroid/trbsoft/userscripts/trb49/db

4) Setting up the ADCs AddOns

The FPGAs that control the ADCs AddOns are initialized and configured with the parameters written in the script (passed as argument in ‘trbcmd’).

Examples of parameters are: number of samples, trigger thresholds, downsampling factor, number of the trigger channels , etc.

→ NOTES:

Note that when called remotely, the startup_TRB49.sh script does not launch the CTS web controller in the end. Is does that operation when it is called in the controller machine directly.

There is a specific script to be executed from remote: startup_TRB49_remotely.sh[3].
[3] This file is also available in the repository https://github.com/jsmarcos/TRB3-GSI-based-DAQ, inside the directory /userscripts_trb49_on_control_unit_OdroidC2
The differences are only two in the remote case: 1) the path for the executable ‘trbcmd’ is explicitly writen and 2) the CTS web controller is not lauched in the end of the script. In remote case, the CTS controller is launched from other script called launch_cts.sh.

Code of the script launch_cts.sh
#!/bin/bash

export DAQOPSERVER=localhost:1 #Check if it is needed

echo "Launching cts_gui"

pkill -f "perl /home/odroid/trbsoft/daqtools/web/cts_gui"
cd /home/odroid/trbsoft/daqtools/web/
/home/odroid/trbsoft/daqtools/web/cts_gui # removed'&' in the end of the line. Jan 2019. JM
#/home/odroid/trbsoft/daqtools/web/httpi localhost 1234 &

#Load CTS configuration
#cd /home/odroid/trbsoft/userscripts/trb49/
#sh ./cts-dump-remotely.sh

Code of the main script startup_TRB49.sh

#!/bin/bash

#sleep 60
cd /home/odroid/trbsoft/userscripts/trb49

#to run the script from the crontab:
if [[ -x ~/.bashrc ]]; then
    chmod a+x ~/.bashrc
fi
PS1='$ '; source ~/.bashrc

DAQ_TOOLS_PATH=~/trbsoft/daqtools
export PATH=$PATH:$DAQ_TOOLS_PATH
export PATH=$PATH:$DAQ_TOOLS_PATH/tools

export DAQOPSERVER=localhost:1

#export TRB3_SERVER=trb012:26000 #change to the respective host name (the same than /etc/hosts)
export TRB3_SERVER=trb049:26000 #change to the respective host name (the same than /etc/hosts)
export TRBNETDPID=$(pgrep -f "trbnetd -i 1")
echo "- trbnetd pid: $TRBNETDPID"

if [[ -z "$TRBNETDPID" ]]
then
    ~/trbsoft/trbnettools/bin/trbnetd -i 1 #starts trbnetd which allows connection with the TRB3; trbnetd -i 1 opens a trbnetd with th$
fi

./check_ping.pl	#ping the TRB, the script must be changed accordingly with the respective TRB name

echo "reset"
./trbreset_loop.pl	#the # of endpoints must be changed accordingly (5 endpoints for 1 TRB)
sleep 1;

trbcmd i 0xffff
#trbcmd s 0x12000002e2d98d28 0x05 0xc001 #CTS TRB12
#trbcmd s 0xcf000003480d8a28 0x00 0xa001 #ADA1
#trbcmd s 0x99000002e30e5728 0x01 0xa002 #ADA2
#trbcmd s 0x4e000002e2e24c28 0x02 0xa003 #ADA3
#trbcmd s 0x6a000002e2e24328 0x03 0xa004 #not used
trbcmd s 0x6a000006e95d3528 0x00 0xC310 #ADC
trbcmd s 0xef000006e95d3228 0x01 0xC311 #ADC
trbcmd s 0xcf000006e95d1b28 0x02 0xC312 #not used
trbcmd s 0xb1000006e9545028 0x03 0xC313 #not used
trbcmd s 0x96000006e95d1828 0x05 0x8000 #CTS TRB49

trbcmd i 0xffff

echo "GbE settings"
loadregisterdb.pl db/register_configgbe.db	#must be changed accordingly (ID of the CTS_FPGA as defined above)
loadregisterdb.pl db/register_configgbe_ip.db	#must be changed accordingly (DAQ_MAC + IP + Dest Port (used in EventBuilder_TRB186.xml))

#echo "TDC settings"
loadregisterdb.pl db/register_configtdc.db	#must be changed accordingly (ID of the TDC_FPGAs as defined above)
#echo "TDC settings end"

#echo "pulser"
# pulser #0 to 10 kHz
# trbcmd w 0xc001 0xa156 0x4e20	# 0x4268 = 17000 -> 170000 ns = 0.170ms -> 5.88 kHz (1ADC + 1 TDC -> 87MB/s, 8% of deadtime)

#echo "pulser enable"
# pulser enable
# trbcmd setbit 0xc001 0xa101 0x2

# JM commented the three commands below, from Alberto/João Saraiva group
#echo "start trigger"
#trbcmd w 0xc001 0xa101 0xffff4000	#enable ch14 (coincidence module 0) trg_channel_mask: edge=1111 1111 1111 1111, mask=0000 0000 0010 0000

#echo "start coincidences with detector 1&3"
#trbcmd w 0xc001 0xa13e 0x30005	#trg_coin_config0: coin_mask=0000 0101, inhibit_mask=0000 0000; window=3 = 30 ns

#echo "limit cts_throttle"
#trbcmd w 0xc001 0xa00c 0x00000401 # cts_throttle: enable=true, stop=false, threshold=1

#Threshold Settings - Below some settings of Alberto/João Saraiva group
#~/trbsoft/daqtools/tools/dac_program.pl ~/trbsoft/userscripts/trb12/thresholds/configFile_a001_40mv
#~/trbsoft/daqtools/tools/dac_program.pl ~/trbsoft/userscripts/trb12/thresholds/configFile_a002_40mv
#~/trbsoft/daqtools/tools/dac_program.pl ~/trbsoft/userscripts/trb12/thresholds/configFile_a003_40mv

#setup ADC addon
Samples=30
SamplesAfterTrigger=60
Threshold_Ch9=80
Threshold_Ch100=220

FPGA="0xC310"
~/trbsoft/daqtools/tools/adc.pl $FPGA init

trbcmd w $FPGA 0xa010 $Samples	#Buffer depth
trbcmd w $FPGA 0xa011 $SamplesAfterTrigger #Samples after trigger
trbcmd w $FPGA 0xa012 1	#Process blocks
trbcmd w $FPGA 0xa013 $Threshold_Ch9	#Trigger offset, invert
trbcmd w $FPGA 0xa014 0 #Readout offset
trbcmd w $FPGA 0xa015 1 #Downsampling
trbcmd w $FPGA 0xa016 8 #Baseline
#trbcmd w $FPGA 0xa017 0x30000000 #Trigger Enable ch31-00
#trbcmd w $FPGA 0xa018 0x0000 #Trigger Enable ch47-32
trbcmd w $FPGA 0xa017 0x30000 #Trigger Enable ch31-00 JM: Hardware channels 16 and 17
trbcmd w $FPGA 0xa018 0x0	#Trigger Enable ch47-32
trbcmd w $FPGA 0xa01a 0x00000000 #Channel disable ch31-00, all channels except ch0
trbcmd w $FPGA 0xa01b 0x0000 #Channel disable ch47-32
trbcmd w $FPGA 0xa01c 0 #Processing mode 0=BlockMode, 1=PSA, 2=CFD
# ignore CFD stuff
#trbcmd w $FPGA 0xa01d 0x340 #CFD delay is 3, CFD window 64=0x40

trbcmd w $FPGA 0xa020 1 #Sum values
trbcmd w $FPGA 0xa021 1 #Sum values
trbcmd w $FPGA 0xa022 1 #Sum values
trbcmd w $FPGA 0xa023 1 #Sum values
trbcmd w $FPGA 0xa024 $Samples #word count
trbcmd w $FPGA 0xa025 0 #word count
trbcmd w $FPGA 0xa026 0 #word count
trbcmd w $FPGA 0xa027 0 #word count

trbcmd w $FPGA 0xa000 0x100 #Reset Baseline

# Second ADC
FPGA1="0xC311"
~/trbsoft/daqtools/tools/adc.pl $FPGA1 init

trbcmd w $FPGA1 0xa010 $Samples	#Buffer depth
trbcmd w $FPGA1 0xa011 $SamplesAfterTrigger #Samples after trigger
trbcmd w $FPGA1 0xa012 1	#Process blocks
trbcmd w $FPGA1 0xa013 $Threshold_Ch100	#Trigger offset, invert
trbcmd w $FPGA1 0xa014 0 #Readout offset
trbcmd w $FPGA1 0xa015 1 #Downsampling
trbcmd w $FPGA1 0xa016 8 #Baseline
#trbcmd w $FPGA1 0xa017 0x30000000 #Trigger Enable ch31-00
#trbcmd w $FPGA1 0xa018 0x0000 #Trigger Enable ch47-32
trbcmd w $FPGA1 0xa017 0x30000 #Trigger Enable ch31-00 JM: Hardware channels 64 and 65
trbcmd w $FPGA1 0xa018 0x0 #Trigger Enable ch47-32
trbcmd w $FPGA1 0xa01a 0x00000000 #Channel disable ch31-00, all channels except ch0
trbcmd w $FPGA1 0xa01b 0x0000 #Channel disable ch47-32
trbcmd w $FPGA1 0xa01c 0 #Processing mode 0=BlockMode, 1=PSA, 2=CFD
# ignore CFD stuff
#trbcmd w $FPGA 0xa01d 0x340 #CFD delay is 3, CFD window 64=0x40

trbcmd w $FPGA1 0xa020 1 #Sum values
trbcmd w $FPGA1 0xa021 1 #Sum values
trbcmd w $FPGA1 0xa022 1 #Sum values
trbcmd w $FPGA1 0xa023 1 #Sum values
trbcmd w $FPGA1 0xa024 $Samples #word count
trbcmd w $FPGA1 0xa025 0 #word count
trbcmd w $FPGA1 0xa026 0 #word count
trbcmd w $FPGA1 0xa027 0 #word count

trbcmd w $FPGA1 0xa000 0x100 #Reset Baseline
# Second ADC Done

#CTS_GUI
echo "Launching cts_gui"
pkill -f "perl $HOME/trbsoft/daqtools/web/cts_gui"
cd $HOME/trbsoft/daqtools/web/
$HOME/trbsoft/daqtools/web/cts_gui &

    #echo "Launching cts_gui"
    #pkill -f "perl /home/odroid/trbsoft/daqtools/web/cts_gui"
    #cd /home/odroid/trbsoft/daqtools/web/
    #/home/odroid/trbsoft/daqtools/web/cts_gui &

#xterm -display :1 -hold -geometry 105x60 +sb -e '$HOME/trbsoft/daqtools/web/cts_gui --noopenxterm'

cd - #JM: to return to the directory in which the previous command was executed
#Load CTS configuration
sh ./cts-dump.sh

→ Perl scripts
/home/odroid/trbsoft/userscripts/trb49/

1. Script check_ping.pl
Checks the avaibility of the communication with TRB3 board (among other things)

2. Script trbreset_loop.pl
Starts by reseting the TRB3 board.
Inquires the name of the available ‘endpoints’ (FPGAs), including the central/controller one (usually called 0x8000).

→ Three Perl databases
/home/odroid/trbsoft/userscripts/trb49/db

1. register_configgbe_ip.db

###########################################################################################
#Eventbuilders:
# EB 0: kp1pc105 eth1 00:1B:21:43:97:EA 192.168.0.2 ports 50000 - 50099

!Register table
# Type # C0 # C1 # C2 # C3 # C4 # C5 # C6 # C7 # C8 #
###########################################################################################
#new memory locations
      0 0x8100 0x8101 0x8102 0x8103 0x8104 0x8105 0x8106 0x8107 0x8108
      1 0x8110 0x8111 0x8112 0x8113 0x8114 0x8115 0x8116 0x8117 0x8118
      2 0x8120 0x8121 0x8122 0x8123 0x8124 0x8125 0x8126 0x8127 0x8128
      3 0x8130 0x8131 0x8132 0x8133 0x8134 0x8135 0x8136 0x8137 0x8138
      4 0x8140 0x8141 0x8142 0x8143 0x8144 0x8145 0x8146 0x8147 0x8148
      5 0x8150 0x8151 0x8152 0x8153 0x8154 0x8155 0x8156 0x8157 0x8158
      6 0x8160 0x8161 0x8162 0x8163 0x8164 0x8165 0x8166 0x8167 0x8168
      7 0x8170 0x8171 0x8172 0x8173 0x8174 0x8175 0x8176 0x8177 0x8178
      8 0x8180 0x8181 0x8182 0x8183 0x8184 0x8185 0x8186 0x8187 0x8188
      9 0x8190 0x8191 0x8192 0x8193 0x8194 0x8195 0x8196 0x8197 0x8198
    10 0x81A0 0x81A1 0x81A2 0x81A3 0x81A4 0x81A5 0x81A6 0x81A7 0x81A8
    11 0x81B0 0x81B1 0x81B2 0x81B3 0x81B4 0x81B5 0x81B6 0x81B7 0x81B8
    12 0x81C0 0x81C1 0x81C2 0x81C3 0x81C4 0x81C5 0x81C6 0x81C7 0x81C8
    13 0x81D0 0x81D1 0x81D2 0x81D3 0x81D4 0x81D5 0x81D6 0x81D7 0x81D8
    14 0x81E0 0x81E1 0x81E2 0x81E3 0x81E4 0x81E5 0x81E6 0x81E7 0x81E8
    15 0x81F0 0x81F1 0x81F2 0x81F3 0x81F4 0x81F5 0x81F6 0x81F7 0x81F8

## Alberto/João Saraiva:
#TRB12: DA7A 32E2D98D 10.0.1.135 ->87
#ODROID: 001E 0634FAB2 10.0.1.67 ->43

## Gamma cameras group - B16
#TRB49 (B16): 02:00:f8:00:be:18 10.0.0.49 -> 49 in Hexadecimal = 31
#ODROID B16: 00:1e:06:36:49:d0 10.0.0.1 -> 1 in Hexadecimal = 1
#JM Laptop: f0:79:59:2f:4e:ee 10.0.0.61 -> 61 in Hexadecimal = 3D
#B16 Linux PC: 14:cc:20:00:6c:61 10.0.0.65 -> 65 in exadecimal = 41

!Value table
# Dest MAC Dest MAC Dest IP Dest Port Src MAC Src MAC Src IP Src Port Packet Size
# Hub # Type # C0 # C1 # C2 # C3 # C4 # C5 # C6 # C7 # C8 #
###############################################################################################################

#0xc001 0 0x0634fab2 0x001e 0x0a000143 50084 0x0634FAB2 0xda7a 0x0a000187 0xc350 0x0578
#0x8000 0 0x063649d0 0x001e 0x0a000001 50084 0xf800be18 0x0200 0x0a000031 0xc350 0x0578
#0x8000 0 0x592f4eee 0xf079 0x0a00003D 50084 0xf800be18 0x0200 0x0a000031 0xc350 0x0578 # JM Laptop
 0x8000 0 0x20006c61 0x14cc 0x0a000041 50084 0xf800be18 0x0200 0x0a000031 0xc350 0x0578 # B16 Linux PC (delta)

2. register_configgbe.db

!Register table
# Type # C0 # C1 # C2 # C3 # C4 # C5 # C6 # C7 # C8 # C9 # C10
###################################################################################
     0 0x8300 0x8305 0x8307 0x8308 0x830b
     1 0x8301 0x8302 0x8304 0x8309 0x830c 0x830e 0x830f 0x8310

!Value table
#	Enable
# SubEvtId UseGbE MultiQueue Trig. Num. InclTrgType
# Hub # Type # C0 # C1 # C2 # C3 # C4
##################################################################################
    0x8000 0 0x8000 1 0 0xffffff 1
# 0xc001 0 0xc001 1 0 0xffffff 1
# 0xc002 0 0x8000 1 0 0xffffff 1

#These values to not need to be written - for completeness only
# SubEvtDec QueDec FrameSize RX enable SubEvtSize Evt/Queue QueueClose MaxQueueSize
# Hub # Type # C0 # C1 # C2 # C3 # C4 # C5 # C6 # C7 #
#######################################################################################################
# 0xff7f 1 0x00020001 0x00030062 0x578 1 59800 200 32000 60000

3. register_configtdc.db

# TDC / ADC config registers

!Register table
# Type # C0 # C1 # C2 # C3 # C4 # C5 #
################################################################
     0 0xc800 0xc801 0xc802 0xc803 0xc804 0xc805

!Value table
# Gnl Conf Trg Window Ch En 1-32 Ch En 33-64 RingBufSize Invert
# TDC # Type # C0 # C1 # C2 # C3 # C4 # C5 #
###########################################################################################

#0xA001	0 0x00000000 0x80640064 0x3fffffff 0x00000000 0x0000007c 0x00000000 # TRISTAN
#0xA002 0 0x00000000 0x80640064 0x3fffffff 0x00000000 0x0000007c 0x00000000 # TRISTAN
#0xA003 0 0x00000000 0x80640064 0x3fffffff 0x00000000 0x0000007c 0x00000000 # TRISTAN

0xC310 0 0x00000000	0x80640064 0x3fffffff 0x00000000 0x0000007c 0x00000000 # ADC1
0xC311 0 0x00000000	0x80640064 0x3fffffff 0x00000000 0x0000007c 0x00000000 # ADC2